## Slide 1: Multiple Antennas and Beamforming
EL-GY 6023. Wireless Communications
Prof. Sundeep rangan

## Slide 2: Outline
Antenna arrays and the Spatial Signature
Receive Beamforming and SNR Gain
Array Factor
Multiple paths and Diversity
Transmit Beamforming

## Slide 3: Antenna Arrays
Antenna arrays: Structure with multiple antennas
  At TX and/or RX
  Key to 5G mmWave and massive MIMO
Two key benefits
Beamforming: This lecture
  Concentrate power in particular directions
  Increases SNR and may enable spatial diversity
  Requires arrays at either TX or RX
Spatial multiplexing: Next lecture
  Enables transmission in multiple virtual paths
  Increases degrees of freedom
  Requires multiple antennas at both TX and RX
IBM 28 GHz array
32 element dual polarized array Sadhu et al, ISSCC 2017
Aurora C-Band Massive MIMO array
64 elements, 5-6 GHz
https://www.taoglas.com/

## Slide 4: Multiple Receive Antennas
Single Input Multiple Output
  One TX antenna
  RX antennas
Transmit a scalar signal
Receive a vector of signals:
What is the channel from to ?
Want channel in complex baseband

## Slide 5: Channel vs. Position
To understand SIMO channel, consider single path channel
  AoA of relative to z-axis
  Delay to origin
  Gain is constant close to origin
Transmit signal and look at response at position
Consider a RX position close to origin
  bandwidth of
Phase rotation with displacement:
  Baseband response at is (proof on next slide):
RX position
Response at
Phase rotation with

## Slide 6: Proof of Phase Rotation with Displacement
Delay of path at is:
Baseband response at :
Also, if
But, by assumption of small displacement:
Hence,
RX position

## Slide 7: Response for a ULA
Uniform Linear array (ULA)
  antenna positions spaced apart
Transmit signal
  Channel single path with AoA , gain
Response at position:
SIMO frequency response is:
Scalar response at
Phase shifts across elements

## Slide 8: Response Decomposition
For a single path channel, the frequency response has two components:
Scalar channel response,
  Response at a reference position in array
Vector spatial signature,
  Vector of phase shifts from the reference
  Also called the steering vector (reason for name will be clear later)

## Slide 9: Array Response in 3D
Many arrays place elements over 2D area
Uniform rectangular array (URA):
  grid of elements
  Spaced and
  Also called uniform planar array (UPA)
Incident angle
  (Azimuth, elevation) or (azimuth, inclination)
Spatial signature:
  complex response to antenna

## Slide 10: Outline
Antenna arrays and the Spatial Signature
Receive Beamforming and SNR Gain
Array Factor
Multiple paths and Diversity
Transmit Beamforming

## Slide 11: Multiple Receive Antennas
Single Input Multiple Output
  One TX antenna
  RX antennas
Transmit a scalar signal
Receive a vector of signals:
Basic question: How do we decode signal from vector ?

## Slide 12: Scalar Multiple Channel Problem
Consider transmission of a single symbol
Receive a vector across channels:
  : Scalar TX symbol
  Vector of channel weights, Vector of noise
Channel can be from many different paths:
  multiple times, frequencies or antennas
Applies to a single degree of freedom (time or frequency)
Question: How do we detect scalar from vector ?

## Slide 13: Linear Combining
RX model:
  1 input, M outputs
Linear combining: Take a linear combination
is called the weighting vector
  Called the beamforming vector for multiple antennas
Creates effective SISO channel:
  1 input 1 output symbol
  Gain:
  Noise:

## Slide 14: Linear Combining Analysis
Linear combining:
  Gain:
  Noise:
Analysis: Let
  average symbol energy
  Assume noise (i.i.d. complex Gaussian noise)
Then, after combining;
  Signal energy
  Noise: is Gaussian with
  SNR is:

## Slide 15: Maximum Ratio Combining
From previous slide: SNR is
Maximum ratio combining: Select BF vector to maximize SNR:
Theorem: The MRC weighting vector and maximum SNR is:
  Any constant can be used. Constant does not matter
  Align BF vector with the channel.
Proof:
  From Cauchy-Schwartz:
  Hence,
  Maximized with

## Slide 16: MRC Gain
SNR with MRC:
SNR on channel is:
Average SNR is:
MRC increases SNR by a factor of relative to average per channel SNR
Beamforming gain =
Example: Suppose average SNR per antenna is 10 dB.
  With antennas and MRC, SNR dB
  Gain increases significantly!

## Slide 17: RX Beamforming
Recall model for a single path channel:
  = spatial signature on that angle, = angle of arrival
  = gain at reference position in array
  = transmitted symbol
RX beamforming is just linear combining across antennas
  is called the beamforming vector
  By convention, we assume
  Geometric interpretation to be given shortly

## Slide 18: MRC Beamforming
Single path channel:
RX beamforming:
SNR per antenna (before beamforming):
  Assume includes only phase shifts
SNR after BF:
MRC beamforming: and
Conclusions:
  Optimal (MRC) beamforming vector is aligned to the spatial signature
  Optimal SNR gain
  Linear gain with number of antennas

## Slide 19: Example Problem
Consider a system
  TX power = 23 dBm with antenna directivity = 10 dBi
  Free space path loss 1000 m
  Sample rate = 400 Msym/s
  Noise energy = -170 dBm/Hz (including NF)
  RX antenna directivity = 5 dBi and 8 elements
Find SNR per antenna and SNR with MRC
Solution: We get a 9 dB gain!

## Slide 20: MATLAB Phased Array Toolbox
Powerful toolbox
Routines for:
  Defining and visualizing arrays
  Computing beam patterns
  Beamforming
  MIMO
  Radar
  …

## Slide 21: Example: Defining a ULA
Define and view the array
Can display array:
  Using viewArray command
  Or, manually

## Slide 22: Computing the Spatial Signature
Compute the spatial signature with the SteeringVector object

## Slide 23: Example: Defining a URA
Define and view the array
Use the phased.URA class
Can compute steering vector similarly
A 4 x 8 URA with normal axis aligned on x

## Slide 24: Multiple Antennas in Commercial Systems
Sub 6 GHz systems: Mostly 1 to 4 antennas on base stations or smart phones
Form factor restricts larger number of antennas
WiFi Router
Linksys AC2200 with 4TX/RX
2x2 LTE base station antenna
Cros-polarization
16 dBi element gain, 90 deg sector 750x120x60mm
K. Zhao, S. Zhang, K. Ishimiya, Z. Ying and S. He, "Body-Insensitive Multimode MIMO Terminal Antenna of Double-Ring Structure," in IEEE Transactions on Antennas and Propagation, vol. 63, no. 5, pp. 1925-1936, May 2015.

## Slide 25: Massive MIMO
Massive MIMO:
  Many base station antennas
  64 to 128 in many systems today
Significant capacity increase
  Typically 8x by most estimates
Use SDMA
  Will discuss this later

## Slide 26: Beamforming and MmWave
To compensate for high isotropic path loss, mmWave systems need large number of antennas
5G handsets: Multiple arrays with 4 to 8 antennas each
5G base stations: 64 to 256 elements
IBM 28 GHz array
32 element dual polarized array Sadhu et al, ISSCC 2017
Huo, Yiming, et al. "Cellular and WiFi co-design for 5G user equipment." 2018 IEEE 5G World Forum (5GWF). IEEE, 2018.

## Slide 27: In-Class Problem: Simple QPSK simulation
Simulate QPSK transmission over a single path channel

## Slide 28: Outline
Antenna arrays and the Spatial Signature
Receive Beamforming and SNR Gain
Array Factor
Multiple Paths and Diversity
Transmit Beamforming

## Slide 29: Array Factor
Suppose RX aligns antenna for AoA
But, signal arrives from AoA
Define the (complex) array factor
  Assume
  Indicates directional gain as a function of AoA
  Dependence on often omitted
SNR gain =
  Max value =
  Usually measured in dBi (dB relative to isotropic)
  Also called the array response
Actual arrival
BF direction
Array

## Slide 30: Uniform Linear Array
Spatial signature (for azimuth angle ):
  Note change from to . (Array aligned on y-axis)
Optimal BF vector for AoA
  (Note normalization)
Array factor:
  ,
Antenna gain:
Arrival
BF direction

## Slide 31: Antenna Gain for ULA
Maximum gain of
Note:
  Endfire vs. broadside
  Beamwidth
Broadside:
Endfire:

## Slide 32: Plotting the Array Factor
Create a SteeringVector object
Get steering vectors
Compute inner products

## Slide 33: Polar Plot
Useful to visualize in polar plot
Note key features:
  Direction of maximum gain
  Sidelobes
  Pattern repeated on reverse side

## Slide 34: Key Statistics
From Jacobs University slides
Values in () for:
Full null beamwidth (zero to zero)
Half power beamwidth (-3dB to -3dB)
First sidelobe level

## Slide 35: Grating Lobes
When
Obtain multiple peaks
Does not direct gain in one direction

## Slide 36: Plotting the Patterns
MATLAB has excellent routines for 3D patterns
Note that this plots directivity not array factor

## Slide 37: Element Gain
Above analysis assumes each element is omni-directional
Each antenna element may also have gain.
Assume all elements of an array are identical and have same orientation
Pattern multiplication theorem: The frequency response of a single path channel is:
Resulting array factor (in linear scale):
  array factor with isotropic elements
Element gain
Spatial signature
Freq response @reference

## Slide 38: Example: URA with Patch Elements
Example 4x8 URA
Add patch element
  Element normal in +x direction
  Peak element gain dBi
  Adds to the total array gain
Isotropic elements
4 x 8 URA
Peak directivity dB
Gain in both positive and negative x direction
Patch elements
4 x 8 URA
Peak directivity dB
Gain low in negative x direction
Element pattern

## Slide 39: Example: URA with Patch Elements in 2D
Pattern multiplication in 2D
Element gain increases directivity
Note: MATLAB plots directivity
  Does not plot array gain
  Directivity is array gain normalized to one

## Slide 40: In-Class Problem: Simulating BF Mismatch
Continue simulation but with BF mismatch

## Slide 41: Outline
Antenna arrays and the Spatial Signature
Receive Beamforming and SNR Gain
Array Factor
Multiple paths and Diversity
Transmit Beamforming

## Slide 42: Multiple Paths
Easy to extend channel response to multiple paths
Each path adds a term with a spatial signature
Time-domain model
Complex gain
Doppler shift
AoA
Delay

## Slide 43: Time-Varying Frequency Response
Apply input
RX vector is
Time-varying frequency response
Vector channel response

## Slide 44: Time-Varying Frequency Response
Multipath channel:
Consider exponential scalar input:
Vector output is:
Time-varying frequency response
May also write:

## Slide 45: OFDM Time-Frequency Grid
Recall OFDM from earlier lecture
Divide channel into sub-carriers and OFDM symbols
  Resource element: One time-frequency point
Data is transmitted is an array:
  OFDM symbol index, = subcarrier index
  One complex value per RE.
Receive a vector:
  One complex symbol per antenna per RE
Subcarrier spacing
OFDM symbol
Time
Frequency

## Slide 46: OFDM Channel with Multiple RX Antennas
OFDM channel acts as multiplication: Under normal operation (delay spread is contained in CP):
OFDM channel gains can be computed from the multi-path components
  OFDM symbol time, sub-carrier spacing
  For each path: Doppler shift, Delay, phase of path, path received energy
RX symbol vectors
Vector channel
TX symbols

## Slide 47: Time Scales
Consider vector channel response
Large scale parameters: Change slowly
  Gain and angles
  Depend on geometry and large obstacles.
Small scale parameters: Change rapidly
  : Changes over frequency on order of inverse delay spread
  : Changes over time on order of Doppler spread

## Slide 48: RX Correlation
How correlated are two different antennas?
  Related to diversity gain
Covariance matrix
Typically fix AoA and path gains, average over and
Averaging over time and frequency: and
  Proof on board

## Slide 49: Correlation with Random AoAs
Suppose:
  ULA with elements
  large. Total power gain
  AoAs spread had pdf
Then:

## Slide 50: Correlation with Uniform AoAs
If uniform
Then:
  distance between antennas
  Bessel function
Become uncorrelated when
Need more spacing for smaller range of angles

## Slide 51: Diversity Gain
Peak gain does not depend on antenna size
High diversity gain requires wide separation
Example:
  GHz
  cm
  Antenna separation m
  Possible in a cellular tower.
  Not possible in a handset

## Slide 52: Outline
Antenna arrays and the Spatial Signature
Receive Beamforming and SNR Gain
Array Factor
Multiple paths and Diversity
Transmit Beamforming

## Slide 53: Multiple TX antennas
MISO channel
  Multiple input single output
  TX antennas, 1 RX antennas
  Transmit vector:
  Scalar RX:
Most of the theory is identical to the SIMO channel

## Slide 54: Single Path Channel
First consider single path channel
Similar to SIMO case, RX signal is:
  path gain
  = angle of departure
  = path delay
  spatial signature
TX and RX spatial signatures are identical
  Except you apply the conjugate transpose
TX array
RX with single antenna

## Slide 55: TX Beamforming
RX signal is:
TX beamforming
  Input scalar information signal
  Create vector signal to antennas:
  is called the TX beamforming vector
Also called pre-coding
TX array
RX
signals
Scalar
TX BF vector

## Slide 56: MRC TX Beamforming
RX signal is:
Analysis is identical to SIMO case
MRC TX BF vector:
  Align with AoD
SNR gain
Define and compute Array Factor similarly
Also define multi-path channel
TX array
RX
signals
Scalar
TX BF vector

## Slide 57: Beamforming and Channel Estimation
Key issue for beamforming: Channel estimation
TX and RX beamforming require that channel is known
We will discuss many of these concepts later
  Reference signals
  Channel feedback
  Channel tracking
  Beam management
  Spatial equalization
TX array
RX array

## Slide 58: Friis’ Law and MmWave
Recall Friis’ Law:
Isotropic path loss decreases with
Millimeter Wave systems: Increases
  Decreases Increase path loss
  Compensate isotropic path loss with directivity,
Fix aperture on TX side, on receiver side
  Can fit antennas on each side
  Leads to directivity:
Can compensate isotropic path loss with directivity

## Slide 59: Friis’ Law and MmWave
Friis’ Law:
Conclusions: With a fixed aperture and beamforming
  Isotropic path loss can be overcome
But systems need very directive beams
  Raises many other issues. E.g. Channel tracking, processing, …
Condition | Directivity scaling | Path loss scaling
No beamforming | constant | 
Beamforming on one side (TX or RX) | constant | constant
Beamforming on both sides (TX and RX) |  | 
Condition | Directivity scaling | Path loss scaling
No beamforming |  | 
Beamforming on one side (TX or RX) |  | 
Beamforming on both sides (TX and RX) |  |