## Slide 1: Antennas and Free Space Propagation
Wireless short course
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Mathematically describe an EM wave:
  Direction of motion, wavenumber, frequency, polarization, …
Identify radio spectrum and power levels used in common commercial wireless products
Perform basic mathematical operations in polar coordinates
  Conversions to cartesian coordinates, rotations, integrals, averages, …
Use tools from MATLAB to compute and plot key antenna parameters
  Directivity, gain, efficiency, …
Compute received power in an angular region using the radiation density and intensity.
Compute the free-space path loss using Friis Law
Derive Friis Law

## Slide 3: Outline
Basics of Electromagnetic Waves
Basics of Antennas
Free Space Propagation

## Slide 4: Electric and Magnetic Forces
Two closely related forces:
  Electric: Forces between charged particles
  Magnetic: Forces between moving charged particles
Forces operate at a distance:
  Enables communication.
  … and many other phenomena in the universe
Represented by a vector field
  Force strength has a direction and magnitude
  Changes with position and time
  E-field: in N/C (force / unit charge)
  B-field: in N/(Am) (force / unit charge / velocity)

## Slide 5: Plane Waves
EM field governed by Maxwell’s equations
All solutions can be decomposed into plane waves
EM plane wave at position
  , speed of light
Sometimes write:
  B
  wave number

## Slide 6: Plane Waves Illustrated
EM plane wave
Five key parameters:
  Amplitude, frequency, direction of motion, phase
  Polarization (see below)
Diagrams on board
  Fixed position, variation in time
  Fixed time, variation in position.
Phasor notation:

## Slide 7: Plane Wave Direction of Motion
EM field constant in plane
Moves along z-direction:
“Poynting” vector:
  Represents “energy flux”
  Energy consumed =
  Units =

## Slide 8: Polarization
Polarization: Orientation of E-field relative to direction of motion
Linearly polarized: Constant orientation
  Vertical:
  Horizontal:
Also, circularly polarized
  Sum of V and H that are out of phase
  Called left hand and right hand
Two degrees of freedom:
  Consider any plane wave in some direction
  Can be decomposed as V + H or LH + RH

## Slide 9: Plane Wave Decomposition
Every electric field is a linear combination of plane waves
Each plane wave in the decomposition has:
  Frequency
  Direction of motion
  Gain, Phase
  One of two polarization
Decomposition can be found from a 4D Fourier transform
  and
  Converts time + space wavenumber and frequency
  Note that there are two polarization components
This decomposition is used in many EM solvers
  And your EM class if you take it

## Slide 10: EM Spectrum
Frequency of EM radiation has wide range
Encompasses many forms of radiation
Radio waves are uniquely valuable since they can propagate far

## Slide 11: Radio Spectrum

## Slide 12: Outline
Basics of Electromagnetic Waves
Basics of Antennas
Free Space Propagation

## Slide 13: Excellent Text for Antennas
This section based on classic text
  Figures are from this text
Balanis, “Antenna Theory”
Full EM theory
Many excellent problems and examples
Designed for RF engineers
We will use only a small portion here
Take an EM class for more!

## Slide 14: Waveguides and Transmission Lines
Transmission lines and waveguides: Any structure to guide waves with minimal loss
Some texts:
  Transmission lines refer to conductors and waveguides to hollow structures
Many examples
Coaxial cable
Waveguide
PCB traces
Microstrip: External layer
Stripline: Internal layer

## Slide 15: Antenna
Transmit antenna: Radiates electromagnetic waves
Converts signals:
  From guided signals in transmission lines to
  To radiation in free space
Receive antenna: Collects EM wave
USRP with four vertical antenas

## Slide 16: Radiation Patterns
Aantenna radiation typically shown via a pattern
  Value of scalar as a function of position
  Antenna usually at origin
  Orientation of the antenna is important
Many possible quantities:
  Power, electric field, …
  Normalized or un-normalized
Can be 2D or 3D
3D
2D

## Slide 17: Spherical Coordinates
Radiation patterns are often given in spherical coordinates
Spherical coordinates:
  Azimuth, counter-clockwise angle in xy plane
  Elevation, angle from xy plane
  Radius from origin
Many texts use polar or inclination angle:
  Use
  Measures angle from z axis
  Most antenna and math texts use polar form
  But, MATLAB antenna toolbox uses elevation form
Remember right hand rule!
Spherical (polar form) Cartesian
Polar coordinates

## Slide 18: Spherical Coordinates in MATLAB
Conversion between spherical and cartesian
Conversion to a coordinate system

## Slide 19: Radians and Steradians
Radian:
  Circle of radius one
  Angle for unit length on circumference
  radians in the circle
Steradian
  Defined on sphere of radius one
  Angles corresponding to unit area on surface
  sr in the sphere
Infinitesimal area and solid angle:
  Note: is the inclination angle not elevation

## Slide 20: Field Regions
Antenna patterns depend on the region
Reactive near field:
  Reactive pattern dominates
Radiating near field or Fresnel region:
  Angular pattern depends on distance
Far field or Fraunhofer region:
  Angular pattern independent of distance
  Radiation is approximately plane waves
Can be approximately calculated using:
  Maximum antenna dimension
  Wavelength

## Slide 21: Rayleigh Distance
Distance to far-field = Rayleigh distance
Most cellular / WLAN systems operate in far field
Ex 1: Half wavelength dipole antenna
  = 2.3 GHz:
  cm
Ex 2: Large cellular base station
  m, = 2.3 GHz
  m
Ex 3: MmWave wide aperture antenna
  cm, = 140 GHz
  m

## Slide 22: Radiation Density
Recall instantaneous energy flux for a plane wave:
  normal vector in direction of the plane wave
Typically consider fields at some frequency :
Time average power
  Note factor of 2
Can write ,
  Radiation density: radiation density
  Maximum power available if aligned in the direction
  Units
  This is a function of position

## Slide 23: Radiation Intensity
From previous slide: Radiation density:
  Units
Also define radiation intensity:
  Watts per solid angle:
In far field, radiation pattern typically decays as:
  In this case,
  Only depends on angular position
  Does not depend on distance

## Slide 24: Total Radiated Power
Total radiated power:
  Units is Watts
  Note term! Angle here is elevation angle not polar angle
Typically measured in dBm or dBW:
  Power relative to mW or W
Review dB calculations if you forgot!
  Ex: A mobile transmitter transmits 250 mW. What is the power in dBm?
  Ans: 250 = 1000/4=. In dBm: dBm

## Slide 25: Typical Wireless Power Transmit Levels
100 kW = 80 dBm: Typical FM radio transmission with 50 km radius
1 kW = 60 dBm: Microwave oven element (most of this doesn’t escape)
~300 W = 55 dBm: Geostationary satellite
250 mW = 24 dBm: Cellular phone maximum power (class 2)
200 mW = 23 dBm: WiFi access point
32 mW = 15 dBm: WiFi transmitter in a laptop
4 mW = 6 dBm: Bluetooth 10 m range
1 mW = 0 dBm: Bluetooth, 1 m range

## Slide 26: Antenna Directivity
Isotropic antenna: Radiates uniformly in all directions
  Theoretically construct
Most antennas concentrate power in certain angles
Antenna directivity:
  [dimensionless]
  Measures power at an angle relative to average
  Average in linear domain is one
Max directivity:
  Directivity in direction with maximum power
Typically measured in dBi
  dB relative to isotropic
Theoretical isotropic antenna
Horn antenna with directivity

## Slide 27: Antenna Gain and Efficiency
Most antennas have losses
Define efficiency:
  Radiated to input power in TX mode
  Remaining power is lost in heat in the antenna
  Note: Some text include losses in the generator
Lossless antenna:
Antenna gain:
  Radiation intensity per unit input power
  For losses antennas, gain = directivity
Radiated power
Input power
Losses / heat

## Slide 28: Antenna Toolbox in MATLAB
Powerful routines for:
  Design and analysis of antennas
  Radiation patterns
Supports many antennas
Accurate EM modeling
Free to NYU students
  Just download it with your MATLAB

## Slide 29: Patterns in MATLAB: Dipole Example
MATLAB has powerful tools for calculating antenna patterns

## Slide 30: Microstrip Patch Example
A more complex antenna
Many other parameters
  Substrate selection (e.g. FR4, Rogers)
  Shapes, notches, …

## Slide 31: Outline
Basics of Electromagnetic Waves
Basics of Antennas
Free Space Propagation

## Slide 32: Antenna Effective Aperture
Suppose RX antenna sees incident plane wave
  Assume polarization aligned to the antenna
The effective antenna aperture (or area):
  Power density of incident wave [W / ]
  Power delivered to load at the receiver [W]
The effective area that the antenna collects
  We will see this is different than the physical aperture
will depend on the direction of arrival

## Slide 33: Aperture and Directivity
From previous slide, effective aperture is:
  Ratio of received power to incident radiation density
Aperture-directivity relation:
  True for all lossless antennas
  Proof: next slide
Consequence: Average aperture is always
  Why?
  Independent of the physical size of the antenna

## Slide 34: Proof of the Aperture-Directivity Relation
Suppose Ant 1 transmits power
Radiation density is:
Received power at Ant 2:
TX from Ant 2, the gain must be the same:
  This is a consequence of reciprocity
Hence, for any two antennas:
From simple antenna calculations for a short dipole:
  (Needs basic EM theory)

## Slide 35: Friis’ Law
Consider two lossless antennas in free space
From previous slide:
From aperture-directivity relation:
This leads to Friis’ Law (for lossless antennas):
  Path loss is proportional to
  Path loss Inversely proportional to proportional to

## Slide 36: Polarization Loss
Friis’ Law assumes incident wave is aligned in polarization
In general, need to consider polarization loss
Recall: polarization vector for a plane wave:
  Direction of the E-field in phasor notation
  A complex vector in 3-dim
Polarization loss factor:
  : Polarization vector of the TX wave from antenna
  : Polarization vector of the RX incident wave
  : Angle between them

## Slide 37: Antenna Impedance and Matching
Not all power from radio may be delivered to antenna
Some is reflected back
Described by reflection coefficient
  Also referred to as
  Complex ratio of forward to reverse wave
Also described by impedance mismatch:
Fraction of power transferred:
Also given as voltage standing wave ratio (VSWR)
Ali et al, Small Form Factor PIFA Antenna Design at 28 GHz for 5G Applications, 2019

## Slide 38: Friis’ Law with Losses
Three losses in practice:
  Polarization loss
  conductive / dielectric loss
  Impedance mismatch
Friis’ Law with lossy antennas:
  : Efficiency of antenna
  : Angle between the polarization vectors
  Note that gain is: