## Slide 1: Non-LOS Propagation and Link Budget Analysis
Wireless short course
Prof. Sundeep rangan

## Slide 2: Learning Objectives
Compute the noise power density given a noise figure
Compute noise figure in a cascade of elements
Relate key parameters of a communication system:
  Bandwidth, coding rate, modulation
Describe communication requirements and perform simple link budget calculations
Qualitatively describe various propagation mechanisms in real world settings
Qualitatively determine which propagation mechanisms are dominant
Compute probabilities of outage from a statistical channel model

## Slide 3: Outline
Noise and Noise Figure
Communication Requirements and Link Budget Analysis
Non-LOS Propagation
Statistical Models for Path Loss

## Slide 4: What is Noise?
Noise: Any unwanted component of the signal
Key challenge in communication:
  Estimate the transmitted signal in the presence of noise

## Slide 5: Types of “Noise”
Internal / thermal noise:
  From imperfections in the receiver
  Thermal noise: From random fluctuations of electrons
  Other imperfections: Phase noise, quantization, channel estimation errors
External Interference
  Signals from other sources
  In-band: Transmitters in the same frequency Ex: Multiple devices in a cellular band
  Out-of-band: From leakage out of carrier
  Some texts do not consider “interference” as noise

## Slide 6: Thermal Noise
Thermal noise: Caused by random fluctuations of electrons
  Typically modeled as AWGN with power spectral density
Units:
  Linear scale = W/Hz = Joules
  Represents energy per degree of freedom = noise energy in any orthongonal sample
  Often written in dB scale: [dBm/Hz]
Fundamental limit determined by statistical physics:
  = Boltzman constant, temperature in Kelvin
  At room temperature (=300 K), dBm/Hz
Practical systems see higher noise power due to receiver imperfections
  Noise figure
  Typical values are 2 to 9 dB in most wireless systems

## Slide 7: NF for Cascade of Elements
Most receivers are built with multiple stages
  Each stage has a gain and noise figure
  Some stages (typically amplifiers) add noise with a noise figure
Total noise figure given by:
  With large initial gain (), init noise figure () is dominant. Must make small.
  Hence usual first stage is a low noise amplifier (LNA)
Gain G1
Thermal noise 1
kTB x NF1
Input power
Pin
Gain stage 1
G2
Additional noise
kTB (NF2-1)
Stage 2
G3
Additional noise
kTB (NF3-1)
Stage 3
Output power
Pout

## Slide 8: Example Problem Molisch 3.1
What is total NF and gain?
Answer: Compute G and NF (in linear units) for each stage:
  Attenuator: NF1=1 (does not add noise), G1=10-0.1(1.5)=0.707 (note sign)
  LNA: NF2=100.1(4)=2.51, G2=10-0.1(10)=10
  Mixer: NF3=100.1(1)=1.25, G3=1 (unit gain)
  Total gain: dB
  Noise figure dB
Attn connector
Loss = 1.5 dB
Low noise amp
Gain = 10 dB, NF = 4 dB
Mixer
Unit gain, NF = 1 dB
Gain G1
Gain G2
NF1
NF2
Gain G3
NF3

## Slide 9: Outline
Noise and Noise Figure
Communication Requirements and Link Budget Analysis
Non-LOS Propagation
Statistical Models for Path Loss

## Slide 10: Communication Requirements
Basic questions:
  How does TX and RX power effect achievable rate for a communication system?
  What level of path loss can a system sustain?
  How much rate can be reliably transmitted?
Answer: We review some basic concepts from Digital Communications
RX
Info rate
TX
Channel gain
Noise PSD
TX power , BW
RX power

## Slide 11: Typical Transmitter Steps
Communication systems typically use three stages
  Channel coding: ex. Convolutional, turbo, LDPC
  Modulation: QPSK, 16-QAM, 64-QAM, …
  Pulse shaping
Determines modulation + coding scheme (MCS)
Info bits Rate =
Coded bits
Channel coding rate
Modulation sym/sec
Complex symbols
DAC + filtering excess BW frac
Baseband
analog
Upconversion
+ Power amp
Power

## Slide 12: Key Transmitter Relations
Information rate:
Signal bandwidth:
Occupied bandwidth:
Ex: A system transmits with rate ½ coding, 16-QAM, 10 Msym/s and excess BW 10%
  Data states: ; (16-QAM); Msym/s;
  Hence information rate is Mbps
  Occupied bandwidth = MHz
Info bits Rate =
Coded bits
Channel coding rate
sym/sec bits/sym
Complex symbols
DAC + filtering excess BW frac
Baseband
analog
Upconversion
+ Power amp
Power

## Slide 13: Receiver Requirements
Power relations
  Power at receiver is
  Noise energy per degree of freedom = Noise PSD:
Requirements at the receiver are typically specified by two key parameters
  SNR per bit (pronounced “ebb-no”) or SNR per symbol:
  Spectral efficiency (Units are bps/Hz or bits/DOF)
The receiver requirements will depend on the MCS and implementation of the receiver
RX
Info rate
TX
Channel gain
Noise PSD
TX power , BW
RX power

## Slide 14: Example Problem
A system uses:
  Convolutional code shown () and , 16-QAM
  Symbol rate Msym/s. No excess bandwidth
  Transmit power: 23 dBm
  RX noise PSD: -170 dBm/Hz (including NF)
For a BER of find the maximum path loss
Solution:
  From graph we need dB
  Information rate is Mbps
  .
  In dB scale: dBm
  Hence, max path loss is dB

## Slide 15: Shannon Capacity
Capacity = max rate achievable given bandwidth and SNR
  Rate optimized over all possible MCSs and communication schemes.
Given by classic Shannon formula
Capacity relates theoretical rate to two key parameters:
  B = bandwidth in Hz
  SNR in linear scale (not dB!!!)
Mathematical result from classic paper in 1948.

## Slide 16: Bandwidth and Power-Limited Regions
Shannon formula:
Power-Limited region:
  As
  Rate linearly increases with power / SNR
Bandwidth-limited region:
  For large SNR,
  Linearly increases in bandwidth,
  Logarithmically increase in SNR.
  Increasing SNR has little practical value

## Slide 17: Actual Rate vs. Shannon Capacity
Theoretical Shannon capacity cannot be achieved
  Needs infinite computation and delay.
Practical modems achieve a rate below Shannon limit.
Useful model:
  D=fraction overhead
  b=loss factor, usually quoted in dB
  Often say “system is b dB below capacity”
  can be thought of as an “effective” SNR
Usually loss from capacity is at least 3dB
  Often higher depending on receiver complexity and other factors

## Slide 18: Rate vs. Capacity Example
What is the maximum rate for a system:
  20% overhead, 10 MHz bandwidth, SNR=12 dB
  Operates at 3dB below Shannon capacity
Answer:
  Effective SNR: dB. In linear scale (since 9=3(3))
  Therefore, Mbps
  Note the final units are in Mbps

## Slide 19: Communication Requirements
Basic questions:
  How does TX and RX power effect achievable rate for a communication system?
  What level of path loss can a system sustain?
Can review in the digital communications class
TX symbols
DAC+ TX filter
Upconversion
ADC +
RX filter
RX symbols
Equalization, demod,
decoding
Info bits
Estimated bits
Coding + modulation
Down-conversion
Pathloss

## Slide 20: Example Link Budget
Link budget: Measures final SNR as a function of TX power and all impairments
Item | Value | Remarks
Transmit power (dBm) | 23.0 | 200 mW transmitter
Distanced based path loss (dB) | 90.0 | Will depend on propagation model
Shadowing (dB) | 20.0 | Will depend on obstructions
Receive power (dBm) | -87.0 | TX power - path loss - shadowing
Bandwidth (MHz) | 20.0 | BW of 802.11 signal
Noise figure | 5.0 | Will depend of implementation of receiver
Noise power (dBm) | -96.0 | -174 +10log(BW) + NF
SNR (dB) | 9.0 | RX pow - Noise pow

## Slide 21: Outline
Noise and Noise Figure
Communication Requirements and Link Budget Analysis
Non-LOS Propagation
Statistical Models for Path Loss

## Slide 22: Propagation Loss with Reflections
In free space, we saw power density decays as
Due to ground reflections, power decays faster than
For d large, decays as = path loss exponent.
  a has been observed from 1.5 to 5.5, but usu. btw 3 and 5.
For single ground reflection, can show =4.
  Based on reflected wave canceling direct wave
  See www.wiley.com/go/molisch Appendix 4-A

## Slide 23: Path Loss Exponent, Coverage & Interference
For coverage-limited systems, low a is good
  Power decays slower => signals have greater range
For interference-limited systems, high a is good
  Ex: If thermal noise is negligible:
Desired signal
Dist = d1
Interfering signal
Dist = d2
P1
P2

## Slide 24: Transmission & Reflection
At any discontinuity in refractive index, incident wave will be transmitted and reflected.
  Angle of incidence = angle of reflection
  Refraction angle determined by Snell’s Law
Amount of reflected and transmitted power:
  Depends on refractive indices of two mediums, angle of incidence and wave’s polarization
Conducting materials may also result in absorption of power

## Slide 25: Transmission Through Typical Materials
Radio waves can transmit through materials, but with attenuation
Source: City of Cumberland, Maryland WiFi study
Building Material | 2.4 GHz Attenuation
Solid Wood Door1. 75" | 6 dB
Steel Fire/Exit Door 1.75" | 13 dB
Steel Fire/Exit Door 2.5" | 19 dB
Brick 3.5" | 6 dB
Concrete Wall 18" | 18 dB
Glass Divider 0.5" | 12 dB
Interior Solid Wall 5" | 14 dB
Marble 2" | 6 dB
Exterior Double Pane Coated Glass 1" | 13 dB
Exterior Single Pane Window 0.5" | 7 dB

## Slide 26: Attenuation Models in MATLAB
MATLAB Phased Array Toolbox has many models atmospheric attenuation
  Commands for free space path loss, and attenuation for fog, gas and rain
  Based on well-studied measurements
Note: Rain fades are particularly important to model for mmWave!
Rain attenuation vs. Freq
10 km distance
Rate rate = 20 mm/hr (very heavy rain)

## Slide 27: Diffraction
Interfering objects (IOs) do not result in sharp shadows.
  Due to wave nature of EM radiation
  Simple ray model is not correct.
Waves diffract at IO boundaries,
  Intensity after IO can be stronger in parts than with no IO!

## Slide 28: Human Blocking at 73GHz Example
0.5 m
1.0 m
1.5 m
2.0 m
2.5 m
3.0 m
3.5 m
4.0 m
4.5 m
5 m
TX
RX
41
42
43
44
45
46
47
48
49
G. R. MacCartney, Jr., S. Deng, S. Sun, and T. S. Rappaport, “73 GHz Millimeter-Wave Human Blockage and Dynamic Measurements,” IEEE VTC 2016
Between 25 and 40 dB blockage
  Depends on distance
Total power predicted by knife edge diffraction
Piecewise linear model used by 3GPP

## Slide 29: Specular Reflections & Scattering
Due to surface roughness, reflected radio waves can be scattered in many directions.
Amount of power loss in specular component related to height of surface irregularities.
Texts provides probabilistic models to estimate power loss based on random height variations.

## Slide 30: Radio Waves Have Many Paths

## Slide 31: Outline
Noise and Noise Figure
Communication Requirements and Link Budget Analysis
Non-LOS Propagation
Statistical Models for Path Loss

## Slide 32: Real Path Loss
Path loss is a complex function of environment
Varies with distance, obstacles, reflections …
Site specific path loss can be predicted with ray tracing
Outputs of commercial WinProp ray tracer

## Slide 33: Statistical Path Loss Models
Model path loss as a random variable
Environmental effects are modeled as random
Model fit for a type of environment
  Eg. Urban, suburban, indoor, … Not site-specific
Based on data
Used for evaluation of performance statistics
  Coverage, rate distribution, …

## Slide 34: Linear Models
Floating intercept model:
  Parameters , fit from data
Used widely in 3GPP, IEEE
  Different models for different scenarios
Caution in any fit model:
  Do not use outside distances, frequencies it was derived
NLOS
LOS
Distance (log scale)
Path loss (dB)

## Slide 35: Related Models
Close in (CI) model
  Match free space at some fixed reference distance
  One less parameter to fit
  Matches true path loss at
Hata model, ….
Multi-slope models
3GPP NLOS / LOS hybrid models

## Slide 36: Outage Probability
Consider transmission with fixed MCS with rate
  No adaptation!
Requires
  Outage: Event that
  Results in zero rate
With variable path loss, , is a random variable
Outage probability: